How to do transit!?!?
Valhalla and OSRM don’t do transit/multimodal, only OTP does (10 routes/second, with topog.).
How to synchronize transit trips, or ensure only one trip. Seemingly impossible in routing, however, if we set each trip duration at 16 minutes (8 minutes of access to/from each station, and decouple stations by transit route), then only one trip per max 30 min route is possible, and this is a solution.
How does a Network run an all-to-all (RW) simulation? How to adapt to Transit?
main_anchors():
NWK.Terminals(k,MAP[k])
NWK._anchor_geometry()
LineStrings = self.hashgrid.geometry(...‘TRs’...)
self.hashgrid.find_one_line(P, ‘TRs’,)
find_one_line(self,point,name_s,d_max,values=None,_scale_test=0.146)
add: values = set(indices where has_duration==0)
Algorithm for adding bus stops (splitting lines) in MAP.
- Transit object contains locations of stops (geo-mounted to map, in meters), and lines (trips) with durations(s).
- We start with a finished MAP object, which contains
len_m	Float32 (N)
lines	LoLu32 (M/N)
seg_len_m	LoLf32 (M/N)
node_x	Float32 (P)
node_y	Float32 (P)
Props	Tuple (N)
property	Dict (39) --> (N) / arrays, list

 on which we can make the following operations:
- add node inside a segment, splitting it in two.
- add node at node of segment, splitting it into two.
- add transit stop node
- add walking segment to transit stop
- add transit segment
What to do with properties:
Have a table of properties that should match the properties in the dict (39), or match without prefix. Transit access and transit will have has_duration, as well as durations forward and backwards set.

NETWORK Data Structure

NW.graph[graph_name] == Class Graph contains:
Variable	Meaning	Format	Size (Sherbrooke)
OATN	Origin-to-anchor TNs assignement	Block	48486 x max 2
OA_s	Origin-to-anchor links time in seconds (walk)	Block	48486 x max 2
OTNs	TNs that are directly connected to an origin	Tuple of integers	8619
OTNix	Maps TNs with entries used by Dijkstra	1darray(uint32)	18052
Oroute	Which anchor to choose in route from O to D.	2darray(uint8)	48486 x 727
DATN	Same for destination		727 x max 2
DA_s	Same for destination		727 x max 2
DTNs	Same for destination		748
DTNix	Same for destination		18045
Droute	Same for destination		48486 x 727
MX_links	Graph connectivity	Numpy sparse matrix
A2Aroute	All-to-all end-to-end Routing results	2darray(float32)	48486 x 727
MX_times	O to D route times	2darray(float32 or 64?)	748 x 18052
MX_prede	O to D route predecessors (used to recover routes!)	2darray(int32) / (value -9999 for end of route)	748 x 18052
LTS_mps	LTS to speed table	dict
max_s	Longest trip (seconds)	float	1800
max_m	Longest trip (m) – not used in routing	float
len	Graph size (# nodes)	int

Consider Sherbrooke: 18052 TNs ; 24416 TRs
Given O and D in (48486 x 727.
Finite trips inside MX_times: 3230622
48486 x 727 = 35,249,322 trips. Out of these, 3,230,622 are finite (9.17%).

PROGRAM FLOW:

Step 1: Build Map and Network from OSM data.
- projekt.main:
  - osmxml.parse_osm(): takes .osm and creates a .dat
  - osmmap.Map(): creates a map object from .dat, saves into .map
  - UrbNet.Network(): created a network object from
The .dat file contains a summary of the relevant data from the .osm XML format, which is slower to parse. The .map file contains an encoding of the osmmap.Map object, which is a representation of the map in flat-earth coordinates around a centre. The UrbNet.Network object is created from the Map object, and concerns itself with the topology of the road network. Notably, it will create other objects:
- TNs: topological nodes, containing each node that is either: a dead end, an intersection, or a transition between two road types. TNs is a subset of all the nodes in the roads in Map.
- TRs: topological roads: each TR starts and ends with a TN, and all links between neighbouring TNs consist of a TR.
- TNs and TRs form the nodes and edges of a graph, which will be instantiated in the simulation studies. Each TR has a physical length (in meters) and also an LTS rating. During a simulation study, the graph matrix is instantiated in the UrbNet.Graph object, which uses a profile from osm.filter.PROFILES to map LTS ratings to speed. The final graph has edge weights measured in time (seconds) – there will be one Graph object per cyclist PROFILE, as different cyclist types will take different routes at different speeds.

Step 2: Simulation Study.

There are several studies that can be performed by this engine, once the osmmap.Map and UrbNet.Network objects are available.

A) Origin-to-Destination Study (One-to-one routing)
In this study, every origin point is assigned exactly one destination point, and each O-D pair is thus routed. It is thus a fast simulation (thousands of routes).

This study requires an Origin-Destination population survey, which suffers from privacy concerns and a small dataset. Our experiments showed that a residence-to-workplace survey gives similar results (correlation above 65%) while providing many more data points and fewer privacy concerns.

B) Residence-to-Workplace Study (All-to-all routing)

Step A1: Get origin-desitnation data: data_loaders.load_reswrk() - takes:
- Name of city
- Census codes (DA)
- UrbNet.Network object

Step A2: Run simulation: study.RW_Study() - takes:

C) Road Segment Study (All-to-all routing)

The procedure is similar to the RW Study.

Step 3: Draw results.

The function call for drawing the map in a browser is projekt.draw(**NWMAP, DRAW_MAP='js'), where NWMAP is the output of projekt.main().

The drawing engine is written in JavaScript, and runs effectively in the Firefox Developer Edition browser, using a JS canvas to draw the image. Drawing is invoked by opening index.html from this browser, which calls the JS code in draw.js and takes in the data to be drawn from Data.jsn (encoded in JSON).